## Slide 1: Arduino & ATmega328
Chia-Wen Chang

## Slide 2: Arduino 前身
Wiring是Hernando Barragán在2003年，於義大利Interaction Design Institute Ivrea（互動設計學院伊夫雷亞，以下簡稱IDII，該校創立於2001年，，2005年被整併退場）進行的碩士論文專案。
該專案的目標是把複雜的電子元件，以簡單易懂的元素呈現，讓藝術家和設計師得以全神專注在創作本身，不受電子學知識的束縛。

## Slide 3: Arduino 出場
2005年，在義大利北方Ivrea鎮的Interaction Design Institute Ivrea任教的Massimo Banzi與David Cuartielles覺得市面上可用的素材與零件(Wring，Basic Stamp..)太過昂貴，學生負擔不起，於是想要打造便宜好用的電子原型平台，萌芽了Arduino Open Hardware這樣的想法。
Arduino的核心開發團隊成員
  Massimo Banzi，David Cuartielles，Tom Igoe，Gianluca Martino，David Mellis 和 Nicholas Zambetti
  http://www.kenleung.ca/portfolio/arduino-a-brief-history-3/

## Slide 4
Arduino是一個open-source的電子開發設計平台，含有容易使用、擴充性強的硬體與軟體，提供給藝術家、設計師、業餘愛好者、任何有興趣的人，建立打造互動式的科技藝術裝置作品。
Arduino提供了簡單好用的I/O介面。
開放源碼(open-source)。
不僅軟體開放源碼，硬體也是開放的。
開發簡單，參考資料多。
可以在Arduino官網免費下載。
Arduino 特色

## Slide 5
UNO
Duemilanove
Mega
Nano
Arduino實驗板(8 bit)

## Slide 6
Arduino DUE
Arduino ZERO
Arduino實驗板(32 bit)

## Slide 7
網路上一些作品(1/3)

## Slide 8
網路上一些作品(2/3)

## Slide 9
網路上一些作品(3/3)
https://www.youtube.com/watch?v=eJg3yuAAawA
https://blog.arduino.cc/

## Slide 10: Introduction
The ATmega48A/PA/88A/PA/168A/PA/328/P is a low power, CMOS 8-bit microcontrollers based on the AVR® enhanced RISC architecture.
PDIP
TQFP
MLF

## Slide 11: Features
Advanced RISC Architecture
  131 Powerful Instructions – Most Single Clock Cycle Execution
  32 x 8 General Purpose Working Registers
  Fully Static Operation
  Up to 20 MIPS Throughput at 20MHz
  On-chip 2-cycle Multiplier
Million instructions per second (MIPS)
Arduino Uno 16MHz

## Slide 12: Features
High Endurance Non-volatile Memory Segments
  32KBytes Flash program memory
  1KBytes EEPROM
  2KBytes Internal SRAM
  Special Microcontroller Features
  External and Internal Interrupt Sources
  Six Sleep Modes: Idle, ADC Noise Reduction, Power-save, Power-down, Standby, and Extended Standby
Code memory
Data memory 斷電消失
Data memory 永久保存
26個

## Slide 13: Features
Peripheral Features
  Two 8-bit Timer/Counters
  One 16-bit Timer/Counter
  Real Time Counter with Separate Oscillator
  Six PWM Channels
  6-channel 10-bit ADC in PDIP Package
  Programmable Serial USART
  Master/Slave SPI Serial Interface
  Byte-oriented 2-wire Serial Interface(I2C)
  Programmable Watchdog Timer with Separate On-chip Oscillator

## Slide 14: Pin Configurations

## Slide 15: Arduino 硬體
https://www.arduino.cc/en/uploads/Main/Arduino_Uno_Rev3-schematic.pdf

## Slide 16: Arduion 與 atmega328P 腳位對應圖

## Slide 17: Block Diagram

## Slide 18: Architecture
the AVR uses a Harvard architecture

## Slide 19: Memory Size

## Slide 20: Status Register
The Status Register contains information about the result of the most recently executed arithmetic instruction.
The Status Register is updated after all ALU operations

## Slide 21: Status Register
Bit 6 – T: Bit Copy Storage
Bit 7 – I: Global Interrupt Enable
Bit 5 – H: Half Carry Flag
Bit 4 – S: Sign Bit, S = N  V
Bit 3 – V: Two’s Complement Overflow Flag
Bit 2 – N: Negative Flag
Bit 1 – Z: Zero Flag
Bit 0 – C: Carry Flag

## Slide 22: General Purpose Register File

## Slide 23: Instruction Execution Timing
the parallel instruction fetches and instruction executions enabled by the Harvard architecture
The Parallel Instruction Fetches and Instruction Executions
Single Cycle ALU Operation

## Slide 24: In-System Reprogrammable Flash Program Memory
Since all AVR instructions are 16 or 32 bits wide, the Flash is organized as 16K x 16
ATmega48A/PA/88A/PA/168A/PA/328/P Program Counter (PC) is 11/12/13/14 bits wide, thus addressing th2/4/8/16K program memory locations.

## Slide 25: SRAM Data Memory
Data Memory Access Times
Data Memory Map

## Slide 26: System Clock and Clock Options

## Slide 27: System Control and Reset

## Slide 28: System Control and Reset
MCU Start-up, RESET Tied to VCC

## Slide 29: I/O-Ports
I/O Pin Equivalent Schematic
提升電阻
保護二極體
All port pins have individually selectable pull-up resistors with a supply-voltage invariant resistance.
All I/O pins have protection diodes to both VCC and Ground

## Slide 30: I/O-Ports
PORTB3 for bit no. 3 in Port B, here documented generally as PORTxn
Three I/O memory address locations are allocated for each port,
  Data Register – PORTx : makes pin LOW or HIGH
  Data Direction Register – DDRx : makes pins input or output
  Port Input Pins – PINx : this is for reading the state of input pins

## Slide 31: Ports as General Digital I/O
B-this is used by digital pin 8 to digital pin 13
C-this is used by analog pins
D-this is used by digital pin 0 to digital pin 7

## Slide 33
DDRB=B11111111; this means that the all the six pins are outputs
DDRB=B11111100; this means that the pins 8 and 9 are inputs and pins 10 to 13 outputs
PORTB=B11111111; this means all pins are HIGH
PORTB=B11011111; this means that pin 13 is LOW

## Slide 34: Example
void setup() {
DDRB=B11100000;//pin 13 is in output mode
}
void loop() {
PORTB=B11100000; //make pin 13 high and power on the led
delay(1000);
PORTB=B11000000; //make pin 13 low and power off the led
delay(1000);
}

## Slide 36
Now if we want to change only a bit we can do this without writing all 8 bits, but only the bit we want to change, and this with SET and CLEAR.
DDRB |= (1<<DDB5)：set-make 1
  or DDRB = DDRB | B00100000
PORTB |= (1<<PORTB5)：set-make 1
  or PORTB = PORTB | B00100000
PORTB &= ~(1<<PORTB5)：clear-make 0
  or PORTB = PORTB & B11011111

## Slide 37: Example – output pin13
void setup() {
DDRB |= (1<<DDB5);//pin 13 is in output mode
}
void loop() {
PORTB |=(1<< PORTB5);//make pin 13 high and power on the led
delay(1000);
PORTB &= ~(1<<PORTB5);//make pin 13 low and power off the led
delay(1000);
}

## Slide 38: EX-01
使用4個LED，接於PORTB
1. 完成1個LED右旋跑馬燈
2. 完成2個LED右旋跑馬燈
3. 完成奇偶數LED燈交替閃爍

## Slide 39: Example – input pin8
void setup() {
//DDRB |= (1<<DDB5) ;//pin 13 is in output mode
//DDRB &=~(1<<DDB0); //pin 8 is in input mode
DDRB = B11111110; //pin 8 input pins 9 to 13 output
Serial.begin(9600);
}
void loop() {
Serial.println((PINB & B00000001));
if ((PINB & B00000001)==1){//
PORTB |=(1<< PORTB5);//make pin 13 high and power on the led
}
else{
PORTB &=~ (1<<PORTB5);//make pin 13 low and power off the led
}
}

## Slide 40: Example – pin10
void setup() {
//DDRB |= (1<<DDB5) ;//pin 13 is in output mode
//DDRB &=~(1<<DDB2); //pin 8 is in input mode
DDRB = B11111011; //pin 10 input pins 8,9,11,12 and 13 output
Serial.begin(9600);
}
void loop() {
Serial.println((PINB&B00000100));
if ((PINB & B00000100)==4){//
PORTB |=(1<< PORTB5);//make pin 13 high and power on the led
}
else{
PORTB &=~ (1<<PORTB5);//make pin 13 low and power off the led
}
}

## Slide 45: EX-02
3個按鈕 + 8個LED
1. 完成 3*8解碼器
2. 完成以下功能
  按鈕001，右旋跑馬燈
  按鈕010，左旋跑馬燈
  按鈕100，霹靂燈
  按鈕110，單數及偶數LED交替閃爍

## Slide 46: External Interrupts
The External Interrupts are triggered by the INT0 and INT1 pins or any of the PCINT23...0 pins

## Slide 47: External Interrupts
An example of timing of a pin change interrupt
INT0 and INT1
  EICRA – External Interrupt Control Register A
  EIMSK – External Interrupt Mask Register
  EIFR – External Interrupt Flag Register
PCINT23...0
  PCICR – Pin Change Interrupt Control Register
  PCIFR – Pin Change Interrupt Flag Register
  PCMSKx – Pin Change Mask Register x (x=0,1,2 )

## Slide 48: External Interrupts
INT0 and INT1
  EICRA – External Interrupt Control Register A

## Slide 49: External Interrupts
INT0 and INT1
  EIMSK – External Interrupt Mask Register
  EIFR – External Interrupt Flag Register

## Slide 50: External Interrupts
Example：
#include <avr/io.h>
#include <avr/interrupt.h>
void setup(){
DDRD &= ~(1 << DDD2); // Clear the PD2 pin
// PD2 (PCINT0 pin) is now an input
PORTD |= (1 << PORTD2); // turn On the Pull-up
// PD2 is now an input with pull-up enabled
EICRA |= (1 << ISC00); // set INT0 to trigger on ANY logic change
EIMSK |= (1 << INT0); // Turns on INT0
sei(); // turn on interrupts
}
void loop() {
}
ISR (INT0_vect)
{
/* interrupt code here */
}

## Slide 51: External Interrupts
PCINT23...0
  PCICR – Pin Change Interrupt Control Register
  PCIE2: Pin Change Interrupt Enable 2 => PCINT[23:16]
  PCIE1: Pin Change Interrupt Enable 1 => PCINT[14:8]
  PCIE0: Pin Change Interrupt Enable 0 => PCINT[7:0]

## Slide 52: External Interrupts
PCINT23...0
  PCIFR – Pin Change Interrupt Flag Register
  PCIF2: Pin Change Interrupt Flag 2 => PCINT[23:16]
  PCIF1: Pin Change Interrupt Flag 1 => PCINT[14:8]
  PCIF0: Pin Change Interrupt Flag 0 => PCINT[7:0]

## Slide 53
PCINT23...0
  PCMSK2 – Pin Change Mask Register 2
  PCMSK1 – Pin Change Mask Register 1
  PCMSK0 – Pin Change Mask Register 0

## Slide 54: External Interrupts
Example：
#include <avr/io.h>
#include <avr/interrupt.h>
void setup(){
DDRB &= ~(1 << DDB0); // Clear the PB0 pin
PORTB |= (1 << PORTB0); // turn On the Pull-up
PCICR |= (1 << PCIE0); // set PCIE0 to enable PCMSK0 scan
PCMSK0 |= (1 << PCINT0); // set PCINT0 to trigger an interrupt on state change
sei(); // turn on interrupts
}
void loop() {
}
ISR (PCINT0_vect)
{
/* interrupt code here */
}

## Slide 55
EX-03：
1. 設置一個指撥開關於Arduino D2，設置一個 LED於D7，當指撥由0撥至1時，改變LED狀態1 次。
2. 設置一個指撥開關於Arduino D3，設置一個 LED於D6，當指撥由1撥至0時，改變LED狀態1 次。
3. 設置一個指撥開關於Arduino D8，設置一個 LED於D5，當指撥狀態改變時(由1撥至0 或 由0撥至1)，改變LED狀態1次。

## Slide 56: 8-bit Timer/Counter0 with PWM
Two Independent Output Compare Units
Double Buffered Output Compare Registers
Clear Timer on Compare Match (Auto Reload)
Glitch Free, Phase Correct Pulse Width Modulator (PWM)
Variable PWM Period
Frequency Generator
Three Independent Interrupt Sources (TOV0, OCF0A, and OCF0B)

## Slide 57: 8-bit Timer/Counter0 with PWM
Timer/Counter0 is a general purpose 8-bit Timer/Counter module, with two independent Output Compare Units, and with PWM support.
It allows accurate program execution timing (event management) and wave generation.

## Slide 58: 8-bit Timer/Counter Block Diagram

## Slide 59: Register
Timer/Counter (TCNT0)
Output Compare Registers (OCR0A and OCR0B) are 8-bit registers.
Interrupt request (abbreviated to Int.Req. in the figure) signals are all visible in the Timer Interrupt Flag Register (TIFR0).
All interrupts are individually masked with the Timer Interrupt Mask Register (TIMSK0).

## Slide 60: Register
The double buffered Output Compare Registers (OCR0A and OCR0B) are compared with the Timer/Counter value at all times.
The result of the compare can be used by the Waveform Generator to generate a PWM or variable frequency output on the Output Compare pins (OC0A and OC0B)
The compare match event will also set the Compare Flag (OCF0A or OCF0B) which can be used to generate an Output Compare interrupt request.

## Slide 61: Register
The clock source is selected by the Clock Select logic which is controlled by the Clock Select (CS02:0) bits located in the Timer/Counter Control Register (TCCR0B).
Timer/Counter (TCNT0)
Output Compare Registers (OCR0A and OCR0B)
Output Compare pins (OC0A and OC0B)
Compare Flag (OCF0A or OCF0B)
Clock Select (CS02:0) bits
Timer/Counter Control Register (TCCR0B)

## Slide 62: Counter Unit
The main part of the 8-bit Timer/Counter is the programmable bi-directional counter unit.
Timer/Counter Overflow Flag (TOV0)

## Slide 63: Output Compare Unit
The counting sequence : WGM01 and WGM00 bits located in the (TCCR0A) and the WGM02 bit located in the (TCCR0B).
Force Output Compare (FOC0x)

## Slide 64
The arduino uno can generate frequencies for PWM pins up to 8Mhz.
For PWM, arduino has three timers one for two pins like:
-timer 0- for pins 5 and 6
-timer 1-for pins 9 and 10
-timer 2-for pins 3 and 11
Beside these registers arduino can put the PWM pin in four modes like
-fast PWM
-phase correct PWM
-frequency and phase correct PWM
-ctc mode

## Slide 65: Fast PWM mode
The fast Pulse Width Modulation or fast PWM mode (WGM02:0 = 3 or 7)
Timer count from a BOTTOM value to a TOP value after that it overflow to BOTTOM value and repeat(sawtooth waveform)
The N variable represents the prescale factor (1, 8, 64, 256, or 1024)
f_clk is the oscillator frequency(16Mhz)

## Slide 66: Phase Correct PWM Mode
The phase correct PWM mode (WGM02:0 = 1 or 5)
timer count from a BOTTOM value to a TOP value after that it not overflow it countdown from TOP value to BOTTOM value and repeat(triangle wave)

## Slide 67: CTC mode
in this mode timer count to a TOP value and when it reach that value clear the timer and execute something. This mode let us to make very precise operation

## Slide 68: Timer/Counter Timing Diagrams

## Slide 69: Timer/Counter Timing Diagrams

## Slide 70: TCCR0A
To choose the fast pwm mode in the TCCR0A we must make the WGM01 and WGM00 bits equals 1

## Slide 71: TCCR0A
TCCR0A=B10100011; this means that the WGM00 and WGM01 from the TCCR0A register are 1 which means that the pins 5 and 6 are in the fast pwm mode.
pin 5
pin 6

## Slide 72: TCCR0B

## Slide 73: TCNT0 & OCR0A

## Slide 74: OCR0B

## Slide 75: Example
  void setup() { pinMode(5, OUTPUT); pinMode(6,OUTPUT); TCCR0A=0;//reset the register TCCR0B=0;//reset the register TCCR0A=0b10100011;// fast pwm mode TCCR0B=0b00000011;// prescaler 64 OCR0A=50;//duty cycle for pin 6 OCR0B=50;//duty cycle for pin 5
  }
  void loop() { // put your main code here, to run repeatedly
  }
we will have a 976 Hz pwm signal
20% duty cycle(ON) and 80%(OFF)

## Slide 76: Example
  void setup() { pinMode(5, OUTPUT); pinMode(6,OUTPUT); TCCR0A=0;//reset the register TCCR0B=0;//reset tthe register TCCR0A=0b11110011;// fast pwm mode TCCR0B=0b00000011;// prescaler 64 OCR0A=50;//duty cycle for pin 6 OCR0B=50;//duty cycle for pin 5
  }
  void loop() { // put your main code here, to run repeatedly
  }
we will have a 976 Hz pwm signal
20% duty cycle(ON) and 80%(OFF)

## Slide 77: Example
  void setup() {
  pinMode(5, OUTPUT); pinMode(6,OUTPUT); TCCR0A=0;//reset the register TCCR0B=0;//reset tthe register TCCR0A=0b01010011;// fast pwm mode TCCR0B=0b00001001;// no prescaler and WGM02 is 1 OCR0A=0;//control value
  }
  void loop() { // put your main code here, to run repeatedly
  }
8Mhz 50%(fixed) duty cycle signal

## Slide 78: Example
if you want a 25kHz (but is at 50% duty cycle) you must choose a OCR0A=39 and a prescaler=8, because if we don’t use prescaler the OCR0A from the formula give us OCR0A=319, and because timer 0 has 8bits the OCR0A <= 255.
void setup() { pinMode(5, OUTPUT); pinMode(6,OUTPUT); TCCR0A=0;//reset the register TCCR0B=0;//reset tthe register TCCR0A=0b01010011;// fast pwm mode TCCR0B=0b00001010;// prescaler 8 and WGM02 is 1 OCR0A=39;//control value
}

## Slide 79: Timer 1
The main difference between Timer 1 and Timer 0 or Timer 2 is that it is a 16 bits timer (instead 8 bits the others) so Timer 1 can count up to 65355 instead to 255. This thing means that Timer 1 has a higher resolution or it can count longer
pins 9 and 10

## Slide 80
TCCR1A it has two of four bits needed to choose the mode of the PWM(fast pwm ,phase correct pwm etc) and the bits who manage the mode to set pins high or low
TCCR1B it has the bits needed to choose the prescaler and the other two bits needed to choose the mode of PWM
OCR1A and OCR1B registers with bits for the duty cycle of the PWM signals for pin 9(OCR1A) and pin 10(OCR1B)

## Slide 82: CTC mode

## Slide 83: Fast PWM mode

## Slide 84: Phase and Frequency correct PWM mode

## Slide 85: Phase correct PWM mode

## Slide 86
In this mode Timer 1 count from a BOTTOM value to a TOP(which can be max in top of the triangle signal or set by OCRnx) value after that it not overflow it countdown from TOP value to BOTTOM value and repeat(triangle wave).
This mode has half of fast PWM mode frequency. It is preferred in motors control.

## Slide 87
Before to choose one of these modes in TCCR1A register are four bits COM1A1,COM1A0,COM1B1 and COM1B0 which controls the pins 9(COM1A) and 10(COM1B).

## Slide 91
If COM1A1 and COM1B1 are 1 that means we generate a signal which frequency is given by the formula fOCnx=fclk/2*N*TOP, where fclk=16MHz, N is the prescaler(given by the CS12,CS11 and CS10 from the TCCR1B register-explain later) and TOP takes the value from the waveform generation mode bit description image(multiple situations).

## Slide 92: Example
void setup() { pinMode(9, OUTPUT); pinMode(10,OUTPUT); TCCR1A=0;//reset the register TCCR1B=0;//reset the register TCNT1=0; TCCR1A=0b01010011;//COM1A0,COM1B0 are 1, COM1A1, COM1B1 are 0 //also WGM11, WGM10 are 1 TCCR1B=0b00010001;//WGM13 is 1 and WGM12 is 0 with no prescaler CS10 is 1 OCR1A=128;// compare value
}
void loop() { // put your main code here, to run repeatedly }

## Slide 93: Example 1KHz
void setup() { pinMode(9, OUTPUT); pinMode(10,OUTPUT); TCCR1A=0;//reset the register TCCR1B=0;//reset the register TCNT1=0; TCCR1A=0b01010011;//COM1A0,COM1B0 are 1, COM1A1, COM1B1 are 0 //also WGM11, WGM10 are 1 TCCR1B=0b00010001;//WGM13 is 1 and WGM12 is 0 with no prescaler CS10 is 1 OCR1A=4000;// compare value
}

## Slide 94: Example
For this mode the TOP value take the 0x03FF value which means 1023 and with the formula fOCnx=fclk/2*N*TOP and no prescaler the resulting frequency is 7820Hz.
OCR1A=512 for a 50%duty cycle
void setup() { pinMode(9, OUTPUT); pinMode(10,OUTPUT); TCCR1A=0;//reset the register TCCR1B=0;//reset the register TCNT1=0; TCCR1A=0b10100011;//COM1A0,COM1B0 are 0, COM1A1,COM1B1 are 1 //also WGM11, WGM10 are 1 TCCR1B=0b00000001;//WGM13ㄝ, WGM12 are 0 with no prescaler CS10 is 1 OCR1A=512;// duty cycle value
}

## Slide 101
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 | #include <PinChangeInt.h> const byte ledPin = 13; volatile byte state = LOW; void setup(){ pinMode(ledPin, OUTPUT); pinMode(A0, INPUT_PULLUP); PCintPort::attachInterrupt(A0, isr, CHANGE); } void loop(){ digitalWrite(ledPin, state); } void isr() { state = !state; }

## Slide 102
2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 | const byte ledPin = 13; volatile byte state = LOW; void setup(){ pinMode(ledPin, OUTPUT); pinMode(A0, INPUT_PULLUP); PCMSK = B00000001; //enable PCINT8 PCIFR = B00000000; // clear all interrupt flags PCICR = B00000010; // enable PCIE1 group } void loop(){ digitalWrite(ledPin, state); } ISR(PCINT1_vect) { state = !state; }